# SG++ OCL Conventions Guide

## Build System Integration
### Rational
As SG++ should have as few dependencies as possible, OCL has to integrated in a way that makes it possible to entirely disable it.
### Implementation
- OCL can be activated by setting “USE_OCL” to “1” in the scons call, e.g. “scons USE_OCL=1”
- OCL sources have to be in their own subfolders with their on SConscript. This SConscript filters the sources if OCL is not enabled, for an example see the kernel “StreamingOCL”
- scons checks if the header “CL/cl.h” and a library “libOpenCL” ire available. To find the header and the library, the environment variables “OCL_INCLUDE_PATH” and “OCL_LIBRARY_PATH” are considered, if they are set by the user.
- For usages of OCL in non-OCL-specific files, the define “USE_OCL” shall be used. This is important for OCL-enabled applications and for the operator factories.
## Parameter Exposure scheme
### Rational
All OCL kernels require parameters (at least for the blocksize), for a better independence from a specific platform, the parameters should be editable without recompilation. To this end, we propose a configuration file scheme that enables this configuration.

### Implementation
- There is one configuration file for every kernel.
- The configuration file controls the platform for the kernel, the load balancing for the kernel, and possibly additional kernel specific options.
- Ideally all parameters can be controlled from the outside. For a floating point precision parameter, templates have to be employed, see the kernel “StreamingOCL” for an example
- Each OCL kernel is associated with a configuration file whose name is unique for the kernel
- The defaults for the configuration file are set up in the kernels operator factory. The configuration is implemented based on the class “OpenCLConfigurationParameters”
## Parameter Name Conventions
### Rational
There are kernel specific parameters and shared parameters that are, e.g. required to manage the platform. To avoid naming conflicts, conventions are estabished
### Implementation
- Kernel specific parameters start with “KERNEL_” and can have an arbitrary suffix
- Resources that are shared by kernel objects are shared using C++11 “shared_ptr”, cloning of the objects takes place at the OpenCL-operation factory